## Slide 1: Analysis of Mobile Opportunistic Networks using All Hops Optimal Paths S. Bayhan*, E. Hyytia, J. Kangasharju* and J. Ott bayhan@hiit.fi http://www.hiit.fi/u/bayhan *University of Helsinki, Finland Aalto University, Finland
Advances in Methods of Information and Communication Technology (AMICT 2014), Petrozavodsk State University, Russia

## Slide 2: Context: mobile opportunistic networks
Mobile devices communicate opportunistically upon contacts
Short range radio: Bluetooth, Wifi Direct, LTE Direct

## Slide 3: Opportunistic communication store-carry-forward

## Slide 4: Outline
Motivation and challenges in opportunistic message routing
Hop-limited routing (how many hops?)
Capacity Analysis of Hop-Limited Routing with Increasing Hop Count
  Step 1: Network topology generation
  Step 2: All Hops Optimal Paths Problem (AHOPs)
Numerical Analysis

## Slide 5: Why opportunistic communication?
No infrastructure or failure in the infrastructure
No dependency on the infrastructure (also avoid being charged)
Hop gain due to direct link between the transmitter and the receiver (power efficiency)
Spectrum reuse gain
Less burden on operator via mobile data offloading
ISP/Service Provider

## Slide 6: Challenges
Q: How to achieve source-to-destination communication?
Time-evolving network topology
Incomplete, inaccurate knowledge
Distributed protocols
Resource-limited mobile devices (e.g., battery, processing power)

## Slide 7: The easiest solution: epidemic routing
Replicate message to every node greedily
Simple! But too much resource usage
How to restrict the resource usage (i.e., bandwidth, number of replications)?

## Slide 8: Hop-Limited Routing
Hop=1
Hop=2
h-hop routing: A message can be forwarded to at most h hops

## Slide 9: Hop-limited routing
Message created
hop=0
Message received
hop=1
hop=2, destination reached
hop=3
hop=10

## Slide 10: How many hops?
Our research questions:
Q1: How is the average time to send a packet from one arbitrary node to another arbitrary node affected by hop restriction h?
Q2: How is the fraction of nodes reachable from one arbitrary node affected by h?
Q3: How is the delivery ratio from one arbitrary node to
another arbitrary node affected by h?

## Slide 11: Capacity Analysis of Hop-Limited Routing with Increasing Hop Count
Motivation and challenges in opportunistic message routing
Hop-limited routing (how many hops?)
Capacity Analysis of Hop-Limited Routing with Increasing Hop Count
  Step 1: Network topology generation
  Step 2: All Hops Optimal Paths Problem (AHOPs)
Numerical Analysis

## Slide 12: AHOP: All Hops Optimal Paths [Guerin and Orda 2002]
If we are given the network topology, we can find the hop-restricted paths on this network.
More formally [Guerin and Orda 2002]:

## Slide 13: AHOP for opportunistic capacity analysis
Q1: Average time to send a packet
Q2: Fraction of nodes reachable
Q3: Delivery ratio
Path length
Size of the connected component
Probability of the existence of a path
s
d
w1
w2
w3
6
4
3
5
2
s
7
1
d
s
w1
w2
w3

## Slide 14: Steps of our analysis
Time Nodeid1 Nodeid2 ConState
T1 n1 n2 up
T2 n3 n6 up
T3 n1 n2 down
Human contact trace
N nodes
AHOP
Analysis
h=1,…,N
Input
Generate the network topology
A sample trace format
Simulate the system
What is our network like, i.e., what is the network topology?
Depends on when/how you look at the network!

## Slide 15: Network topology generation
Approach 1: Aggregate all contacts in the trace, and create a static graph to represent network topology  Static graph
T=0
T
A
B
C
B
C
E
t1
t2
t3
D
B
t4
A
B
C
E
D
Approach 2: Instead of one single graph, observe the network in several time points, and create the network topology  Time-aggregated graph
A
C
B
D
E
A
C
B
D
E
Time interval 1
Time interval 2
t3 t4
t1 t2

## Slide 16: Static vs. Time-Aggregated graphs
Time-aggregation results in loss of temporal dynamics but simplistic
Static graph overestimates the connectivity and hence the capacity
How much does it affect?
A
B
C
E
D
A
C
B
D
E
A
C
B
D
E
Time interval 1
Time interval 2
Static graph
D  B  C  E in static graph
Only D  B in this second graph
B C link is missing

## Slide 17: AHOP analysis
Human contact trace
N nodes
AHOP
Analysis
h=1,…,N

## Slide 18: Optimal paths Path weight: additive or bottleneck
w(p) = w(A,B) + w(B,C) + w(C,D)  Additive weights
w(p) = max{w(A,B), w(B,C), w(C,D)}  Bottleneck weights
A
B
C
D
w(A,B)
w(B,C)
w(C,D)
p: A  B  C  D
Guerin and Orda [TON2002] show that
  Bellman-Ford provides the lower bound for additive weights: O(h|E|)
  A lower complexity algorithm exists for bottleneck weights: O(|E|log(N) + h(N^2/log(N))
Optimal path p* from A to D is the path with minimum w(p) among all paths from A to D.
Hop-limited optimal path p* is ph* where length(ph*) <= h
Given the edge weights, what is the weight of p, w(p)?

## Slide 19: AHOP for hop-limited routing
Additive weight: Path weight  routing delay
weight of an edge: inter-contact time between the corresponding nodes
Bottleneck weight (capacity): A routing scheme should choose the paths that will highly probably exist  most probable paths.
weight of an edge: the inverse of the number of encounters between the corresponding nodes
with minimum w(p)

## Slide 20: Numerical Evaluation
R for network topology generation (timeordered package) and AHOP analysis
  Timeordered by Benjamin Blonder: http://cran.r-project.org/web/packages/timeordered/index.html
ONE for simulations ONE: http://www.netlab.tkk.fi/tutkimus/dtn/theone/

## Slide 21: Human contact traces
http://crawdad.cs.dartmouth.edu/
Community Resource for Archiving Wireless Data At Dartmouth

## Slide 22: Static analysis: hop limit vs. capacity
Delivery ratio increases while delay decreases with increasing h
Marginal changes
after these points

## Slide 23: Static analysis: optimal hop count

## Slide 24: Answers to our research questions
Q1: Average time to send a packet
Nodes can be reached faster by relaxing hop count
Improvement vanishes after several hops
Optimal hop counts (total path delay): Infocom05 (3 hops), Cambridge (2 hops), and Infocom06 (2.6 hops)
Q2: Fraction of reachable nodes
The first two hops are sufficient to reach every node from every other node.
Q3: Delivery ratio
increases significantly if at least two hops are allowed, and stabilizes after h approx 4.

## Slide 25: Time-aggregated graphs
Three aggregation time windows:
Short : 1 h,
Medium: 6 h,
Long: 24 h

## Slide 26: Time-aggregated graphs Optimal hop count over time
Infocom05 trace:
  1 hour time intervals, 70 samples
Dependency on the time of the day
Lower than static optimal hop count
Small world network

## Slide 27: Time-aggregated graphs Hop count vs. reached fraction of nodes
Larger time-window, higher reached fraction
Acc. to static analysis, 2 hops are enough to reach all. But lower connectivity for others.
Trend is the same (h=2 achieves most of the gains of multi-hop routing).

## Slide 28: Analysis on the network snapshots Hop count vs. capacity
Highest increase from h=1 to h=2
After h=4, vanishingly small gain

## Slide 29: Analysis of the actual operation Hop count vs. delivery ratio
Agrees our previous analysis.
Trend is the same (h=2 achieves all the gains of multi-hop routing).

## Slide 30: Analysis of the actual operation Delivery delay and path lengths
TTL independency
Agrees our additive capacity results
Infocom06
Infocom05

## Slide 31: Summary
Capacity of the studied human contact networks increases significantly with h>=2
Improvement vanishes after h=4
Static graph approach overestimates connectivity and performance
Time window of the aggregation should be paid attention to
A more generic framework for opportunistic networks (different than small world networks)

## Slide 32: Follow our research from http://www.netlab.tkk.fi/tutkimus/pdp/ Reach us at:
bayhan@hiit.fi
esa@netlab.tkk.fi
jakangas@helsinki.fi
jo@netlab.tkk.fi
Thank you.

## Slide 33: Reading list
Guérin, Roch, and Ariel Orda, "Computing shortest paths for any number of hops." IEEE/ACM Transactions on Networking (TON) 10.5 (2002): 613-620.
Burdakov, Oleg P., et al. Optimal placement of communications relay nodes. Department of Mathematics, Linköpings universitet, 2009.
S.Bayhan, E.Hyytia, J.Kangasharju, and J. Ott, Analysis of Hop Limit in Opportunistic Networks by Static and Time-Aggregated Graphs, submitted to IEEE ICC 2015.
M. Vojnovic and A. Proutiere, “Hop limited flooding over dynamic networks,” in Proceedings IEEE INFOCOM, 2011, pp. 685–693.
B. Blonder, T. W. Wey, A. Dornhaus, R. James, and A. Sih, “Temporal dynamics and network analysis,” Methods in Ecology and Evolution, vol. 3, no. 6, pp. 958–972, 2012.
A. Casteigts, P. Flocchini, W. Quattrociocchi, and N. Santoro, “Time-varying graphs and dynamic networks,” Int. Journal of Parallel, Emergent and Distributed Systems, vol. 27, no. 5, pp. 387–408, 2012.